## Slide 1: A novel multi-set data analysis approach for enhancing industrial process understanding and troubleshooting
Raffaele Vitale, Onno E. de Noord, Johan A. Westerhuis, Age K. Smilde, Alberto Ferrer
Notes: Good afternoon everybody, my name is Raffaele Vitale and I am currently working as a PostDoc associate at the University of Lille, in France. However, the present work was carried out during my Ph.D. period at the Universitat Politècnica de València under the supervision of Prof. Alberto Ferrer and Mr. Onno de Noord from Shell Global Solutions, and in collaboration with Dr. Johan Westerhuis and Prof. Age Smilde from the University of Amsterdam. Its main aim was the development of a novel strategy for the tentative identification of the number of common and distinctive components in multi-set data analysis.

## Slide 2: Multiple sources of data
Common components are related to processes taking place in all the data blocks under study
Distinctive components are related to processes taking place in only one or few of the considered data blocks
Notes: In many research and practical domains, it has recently become quite frequent to exploit multiple analytical platforms to comprehensively study the same system of interest. For example, it is rather common nowadays to monitor a chemical process by at the same time i) collecting samples from the reaction medium during its progress and subjecting them to specific laboratory tests, ii) following the time evolution of so-called process or engineering variables, like temperatures, pressures or flow rates, measured by particular sensors installed inside the reactor, and iii) recording spectroscopic data in-line through advanced fibre optic-based instrumentations. In these cases, an intriguing and challenging task would be to distinguish the common and distinctive components underlying for instance two of the various sets of data, resulting from the application of the different characterisation techniques, where by common components one refers to events affecting all the concerned data blocks and by distinctive components those affecting only one of them (or few of them if more data blocks are investigated). But in which contingencies such data blocks can be (let’s say) concatenated and analysed in this fashion?

## Slide 3: State of the art
Smilde, A. et al., J. Chemometr., 2017 (31), e2900
van der Kloet, F. et al., BMC Bioinformatics, 2017 (17), 271-286
Van Deun, K. et al., Chemometr. Intell. Lab., 2013 (129), 40-51
Simultaneous Component Analysis (SCA);
DIStinctive and COmmon Simultaneous Component Analysis (DISCO-SCA);
Adapted Generalized Singular Value Decomposition (Adapted GSVD);
ECO-POWER;
(Generalized) Canonical Correlation Analysis (CCA);
O2PLS
Many dimensionality reduction methods, which model simultaneously all the data blocks under study, have been proposed to retrieve common and distinctive processes underlying them:
None of them encompasses computational steps to determine the number of common and distinctive components
Notes: In the last decades, many dimensionality reduction methods have been proposed to model the common and distinctive components underlying the different data blocks under study when dealing with multi-set problems. This is a list of some of the most commonly used of these approaches, which have been recently compared by Katrijn in this article. These techniques can be classified according to their capability of handling either object-wise or variable-wise linked data structures or retrieving or not the distinctive components affecting the variability of only several of the concerned data blocks. However, they all share the same limitation: none of them encompasses preliminary computational steps aimed at identifying the number of such common and distinctive components, which in most cases, can jeopardise the stability and therefore the interpretation of the final results. Is there then a way to get an at least indicative idea of such a number?

## Slide 4: Data analysis strategy
CCA
2. PCA-CCA
4
3. Common components
(SVD on X1TX2)
4. Distinctive components
of X1
(SVD on X1 after deflation)
4. Distinctive components
of X2
(SVD on X2 after deflation)
1. Effective rank of X2
1. Effective rank of X1
X1
X2
N
N
J1
J2
U1
N
A1
U2
N
A2
Vitale, R. et al., J. Chemometr., 2021 (35), e3266
Vitale, R. et al., J. Chemometr., 2017 (31), e2937
Notes: This is our proposal. Suppose we want to recover the information associated to the common and distinctive components of two data blocks sharing the row dimension, say X1 and X2. Under the assumption that the common components are those showing the highest between-block correlation (either positive or negative), their number can be tentatively identified by Canonical Correlation Analysis. Specifically, by a permutation test-based approach based on Canonical Correlation Analysis, that I am going to present in the next slides. Unfortunately, CCA suffers from severe limitations when the number of rows of X1 and X2 is lower than the number of their columns. In order to overcome such limitations, CCA can be directly run on the scores proceeding from a preliminary PCA decomposition of X1 and X2. But to this end, the effective rank of these two matrices has to be precisely determined to prevent noisy components to be involved in the CCA computational procedure, which might lead to detect spurious correlations between X1 and X2. A permutation test-based strategy is also proposed to address such a task. Once determined the number of common components, their profiles can be retrieved by one of the aforementioned techniques. Here, the focus will not be on how to model such components, but on how to determine their number. Nevertheless, to get some insights into the information they carry, we tried to use a pseudo-O2PLS methodology, by which these common factors are extracted by executing a truncated Singular Value Decomposition of the between-block covariance matrix X1TX2. The distinctive components can be then explored by performing PCA by SVD separately on X1 and X2 after deflating the common ones. Also their number can be identified by the same method used before for the effective rank determination of the single data blocks. I want to stress once again that here the focus is on the determination of the number of common and distinctive components underlying X1 and X2 not on the retrieval of their profiles and that the described pseudo-O2PLS methodology represents just an easy way to get a very general idea of the intrinsic information they carry and on the actual power of the developed strategy.

## Slide 5
Variable #2
Variable #1
…
Batch-wise
unfolding
Variables
Batches
Timei
Multi-synchro
A Shell 6-stage chemical process data
González-Martínez, J.M. et al., J. Chemometr., 2014 (28), 462-475
Notes: To test the feasibility of this novel approach for a real-world application, we decided to apply it to a dataset related to a Shell 6-stage chemical batch process and consisting of a certain number of variables (mainly temperatures, pressures and flow rates) recorded over time during the evolution of different batch runs. Prior to the analysis, variable trajectory synchronisation was performed by a recently proposed algorithm, Multi-synchro, to guarantee all such runs had the same evolution pace. The complete three-way array was then unfolded batch-wise into a matrix whose rows contain the whole time evolution of all the concerned variables for the various batches.

## Slide 6
Data blocks separation
Batches leading to a gradually lower and fluctuating product quality
NOC batches
X1
X2
Common (in-control) variability
Distinctive
(out-of-control)
variability in X2
Notes: Afterwards, the unfolded data matrix was split into 2 different blocks, namely X1 and X2. X1 contained information associated to batches which evolved under Normal Operating Conditions. On the other hand, the runs in X2 were found to lead to products with a gradually lower and fluctuating quality. What do we want to find out here? Well, assuming that the distinctive variation in X2 is due to a possible deviation from NOC, the idea is to first identify the number of common components shared by X1 and X2 and supposedly describing the in-control variability of the process, filter them from X2 and then try to determine the root causes of such a deviation exploring it after its deflation. As here the common dimension between the two data blocks is the column one, the analysis was carried out by transposing X1 and X2 after preprocessing.

## Slide 7
Shell process data: common and distinctive component number
X2
X1
1 common component
Notes: 2 and 5 components were isolated from X1 and X2, respectively. A single common component was detected by the CCA-based permutation test.

## Slide 8
Shell process data: first distinctive component loadings of X2
8
in-control; out-of-control
Notes: Since the attention is focused on the distinctive variability of X2, the figure displays the loadings of the first distinctive component for this block (found to be statistically significant after running again the permutation-based effective rank estimation test). The loadings are divided in distinct subplots, each related to the evolution of one of the 21 measured variables over time. The vertical dotted lines separate the 6 stages of the process. Not all the variables were active in these stages, that’s why part of some loadings trajectories is missing. Among those showing a consistent non-zero temporal trend and then a consistent contribution to this component, variables #1, #12, #13 and #14 exhibited both a higher variability and a higher average level in the out-of-control batches than in the in-control ones. These were also pointed out as those most affected by a possible ongoing fault using different diagnostic tools in a preliminary exploratory analysis of such data.

## Slide 9: Combining data from two reacting units
X1
X2
X1
X2
Common
variability
Distinctive
variability
Common
variability
Distinctive
variability
Common
within-distinctive
variability
Distinctive
between-distinctive
variability
Distinctive
between-distinctive
variability
Unit 1
Unit 2
Notes: What if more than two datasets have to be dealt with? What we tried to do was to extend the developed approach for hierarchical common and distinctive component identification. The product quality issue was actually a bit more complicated than as described before. Such a product in fact is produced in two different reacting units and then stored in a single container before being sold. As the same data structure was available for both these reacting units, apart from evaluating the nature of the common and distinctive components within every one of them, it would be also interesting to assess whether the distinctive variability for X2 in Unit 1 and the distinctive variability for X2 in Unit 2, which are both plausibly related to a possible deviation from NOC, share something or not. As interesting would be to additionally assess what is unique in such distinctive variations.

## Slide 10: Combining data from two reacting units
X1
X2
X1
X2
Common
variability
Distinctive
variability
Common
variability
Distinctive
variability
Common
within-distinctive
variability
Distinctive
between-distinctive
variability
Distinctive
between-distinctive
variability
Unit 1
Unit 2
Notes: What if more than two datasets have to be dealt with? What we tried to do was to extend the developed approach for hierarchical common and distinctive component identification. The product quality issue was actually a bit more complicated than as described before. Such a product in fact is produced in two different reacting units and then stored in a single container before being sold. As the same data structure was available for both these reacting units, apart from evaluating the nature of the common and distinctive components within every one of them, it would be also interesting to assess whether the distinctive variability for X2 in Unit 1 and the distinctive variability for X2 in Unit 2, which are both plausibly related to a possible deviation from NOC, share something or not. As interesting would be to additionally assess what is unique in such distinctive variations.

## Slide 11: Unit 1 + Unit 2: common within-distinctive component
Unit 1
Unit 2
in-control; out-of-control
Notes: Only one common within-distinctive component was isolated by running again the whole approach after the first analysis round performed unit-wise. As expected, since the common component retrieval is based on a pseudo-O2PLS procedure, the loadings profiles are very similar between units but not identical. They however highlight variable #1 (at least from stage #2 on) is that featuring the most consistent contribution to this factor over time. Such a variable could constitute then the common problem affecting both the reacting units.

## Slide 12: Combining data from two reacting units
X1
X2
X1
X2
Common
variability
Distinctive
variability
Common
variability
Distinctive
variability
Common
within-distinctive
variability
Distinctive
between-distinctive
variability
Distinctive
between-distinctive
variability
Unit 1
Unit 2
Notes: What if more than two datasets have to be dealt with? What we tried to do was to extend the developed approach for hierarchical common and distinctive component identification. The product quality issue was actually a bit more complicated than as described before. Such a product in fact is produced in two different reacting units and then stored in a single container before being sold. As the same data structure was available for both these reacting units, apart from evaluating the nature of the common and distinctive components within every one of them, it would be also interesting to assess whether the distinctive variability for X2 in Unit 1 and the distinctive variability for X2 in Unit 2, which are both plausibly related to a possible deviation from NOC, share something or not. As interesting would be to additionally assess what is unique in such distinctive variations.

## Slide 13: Unit 1 + Unit 2: first distinctive between-distinctive components
Unit 1
Unit 2
Notes: The loadings profiles of the first distinctive between-distinctive component (found to be statistically significant after executing again the permutation-based effective rank estimation test) are here shown. Characteristic patterns of variables, some of them already spotted by classical diagnostic tools, were found to be characterised by loadings with a consistent non-zero trend over time for both Unit 1 and Unit 2. These variables might have been affected by a specific event occurring in the respective concerned unit. It is also important to notice that variable #1 from stage #2 on feature practically zero and non-consistent loadings for both Unit 1 and Unit 2 (which is a good sign in relation with what displayed in the previous slide).

## Slide 14: Conclusions
A novel approach for identifying and modelling common and distinctive components underlying two blocks of data was proposed
Satisfactory results were obtained in a real industrial case-study
Additional tests were successfully carried out on spectral and biological datasets
A comprehensive comparison between this strategy and other methods for common and distinctive component analysis (e.g., O2PLS and JIVE) will be carried out in the near future
Notes: In conclusion, a new approach for identifying the number of common and distinctive components underlying two blocks of data was proposed. The retrieval of the profiles of these components was carried out by a pseudo-O2PLS computational strategy just to have a tentative idea on the information they carry and on the actual power of such a novel methodology. Pretty satisfactory results were obtained in a simulated pseudo-spectral and a real industrial case-study, and additional tests (whose results were not shown in this presentation) were successfully performed on real spectral and biological dataset. A hierarchical extension of such an approach to cope with more than two blocks of data was also proposed and its potential preliminarily assessed. As a next step, the potential of combining the developed strategy with other methods for common and distinctive component analysis like JIVE and proper O2PLS has to be evaluated.

## Slide 15: Thanks for your attention