## Slide 1: Bayesian Hierarchical Modeling for Large-Scale Sensors Deployments and Applications
Anna Ballario1,2, Francesca Pennecchi1, Alessandro Schiavi1, Andrea Prato1
1INRiM – Istituto Nazionale di Ricerca Metrologica
2PoliTo – Politecnico di Torino
ENBIS Spring Meeting 2026
Granada, May 27-28, 2026

## Slide 2: Introduction
Millions of low-cost sensors being produced weekly:
  impossibility to apply standard calibration procedures
  large-scale calibration methods need to be introduced
Statistical methods:
  in-lab calibration of a small sample and virtual calibration of the entire batch
  number of required experimental (“in-lab”) calibrations reduced
  CONS: increased uncertainty and less reliability
2

## Slide 3: Virtual Calibration
Exploiting data from a reference, fully in-lab calibrated lot of N sensors
  mixture distribution of N Normal(Si, u(Si)) modeling the sensitivities of the reference lot
  determination of an interval of acceptable sensitivity values [Slow(p), Sup(p)]
For any new lot from the same production, in-lab calibration of a small sample of sensors n << N
Bayesian inference on the remaining N-n sensors
Evaluation of the reliability and estimation of sensitivity

## Slide 4: A Bayesian model
Binomial prior to model the number of defective sensors C in the whole lot
Hypergeometric likelihood on the number of defective items k in the sample of size n
Conjugate model: Binomial posterior with updated parameters

## Slide 5: A metric for the reliability
A metric for batch reliability is defined based on posterior cumulative probability:
Figure. Variation of the probability as a function of n
95 % of reliability with:
at least n = 1630
max k = 49

## Slide 6: Hierarchical extension
Introduction of a Beta hyperprior on the probability p of defective sensors
  direct integration of prior industrial knowledge
  explicit control over parameter variability
  improvement in flexibility and robustness of the reliability
CRUCIAL STEP: elicitation of hyperprior parameters to ensure the model coherently and accurately reflects prior knowledge
Figure. Comparsion of the posterior distribution for different Beta hyperprior

## Slide 7: Sensitivity estimate and uncertainty evaluation
Mixture distribution to model the sensitivity:
  [Slow (p), Sup (p)]: limits of an interval encompassing the (1 − p) fraction of acceptable sensors
  [Smin, Smax]: maximum and minimum of the distribution
Sunk is the variable to be estimated, arises from a mixture of:
  a rectangular distribution on [Slow (p), Sup (p)]
  a U-shaped distribution on [Smin, Smax]
Weights of the mixture:-
  : fraction of ’good’ sensors
  : fraction of defective sensors

## Slide 8
  Sensitivity:
  Uncertainty:
  where pd= (D = d)
Figure. Value of the uncertainty as a function of p

## Slide 9: Case study
100 nominally identical MEMS calibrated at INRiM
Dataset randomly split: 50 benchmark — 50 unknown batch
Acceptance interval:
[Slow, Sup] = [833.18, 849.14] (for p = 0.06)
Wider range for uncertainty evaluation:
[Smin, Smax] = [827.69, 855.06]
Estimate of the sensitivity: Sunk = 841.16 D16-bit-signed/(ms-2)
n = 5, k = 0 sensors counted outside acceptance interval
True number of defective sensors: C = 0
Prior model | Mean | Mode | Reliability | u(Sunk)
Beta(0.06, 0.94) | 0.4 | 0 | 0.959 | 4.684
Beta(0.6, 9.4) | 1.8 | 0 | 0.821 | 4.910
Beta(6, 94) | 2.6 | 2 | 0.730 | 5.035
Beta(60, 940) | 2.7 | 2 | 0.717 | 5.054
Original Model | 2.7 | 2 | 0.717 | 5.056

## Slide 10
Industrial impact: drastically reduced times and costs for sensors network deployment while maintaining traceability
Hierarchical modeling insight: better captures prior information structure, but highly sensitive to hyperparameter choice; weakly informative priors may lead to high reliability while increasing posterior variance
A decision framework employing utility functions is under development to provide optimal sampling plans while keeping into account posterior variance
Conclusion

## Slide 11
References
[1] A. Prato, F. Pennecchi, G. Genta and A. Schiavi, A Bayesian statistical method for large-scale MEMS-based sensors calibration, Metrologia 61 (2024) 015005
[2] Prato A, Mazzoleni F and Schiavi A, Traceability of digital 3-axis MEMS accelerometer: simultaneous determination of main and transverse sensitivities in the frequency domain, Metrologia 57 (2020) 035013
[3] Ballario A., Prato A., Schiavi A., Pennecchi F., Bayesian Hierarchical Modelling for Large-Scale Sensor Calibration, submitted to Quality and Reliability Engineering International, under review

## Slide 12: Thank you for the attention!