## Slide 1
Enhancing photogrammetric measurement systems through Gaussian Splatting
Mattia Trombini, Giacomo Maculotti Gianfranco Genta, Maurizio Galetto
Presenting author Mattia Trombini Dept. of Management and Production Eng., Politecnico di Torino, Italy mattia.trombini@polito.it
Firenze, 8th September 2026

## Slide 2
02
Agenda
Introduction
Problem statement
Methodology
Innovative approach
Experimental setup
Discussion and conclusions
Enhancing photogrammetric measurement systems through Gaussian Splatting
M. Trombini, G. Maculotti, G. Genta, M. Galetto
8th September 2026

## Slide 3
Photogrammetry fundamentals
From images to metric 3D geometry
INTRODUCTION
/
MACHINE VISION AND PHOTOGRAMMETRY
Acquisition
Physical Images
Point Cloud
Dense Geometry
Mesh
Surface Model
Ray 1
Ray 2
Camera i
Camera j
Structure-from-Motion (SfM)
Definition
Image-based technique using (affordable) cameras to generate high-detail 3D dense point clouds and textured meshes.
Alignment
Based on collinearity equation. A single view gives direction; multiple views (at least 2) allow intersection to find 3D coordinates (X, Y, Z).
Key process steps
Feature Extraction (keypoints)
Matching (tiepoints)
Dense reconstruction (MVS)
Calibration
Requires solving internal parameters (focal length, distortion) and external parameters (pose) for metric accuracy.
03
Enhancing photogrammetric measurement systems through Gaussian Splatting 8th September 2026

## Slide 4
Static-in-time inspection
Static reconstructions and coverage gaps
PROBLEM STATEMENT
/
PROBLEM DEFINITION
KEY LIMITATIONS
Density of reconstruction
Low
High
CONCEPT OF STATIC-IN-TIME
Conventional photogrammetry loses the temporal dimension.
04
Local Incompleteness
Dense point clouds fail in regions where image coverage is insufficient or angles are suboptimal.
Bound to t0
Information is frozen at the acquisition instant. The physical state cannot be revisited once access is lost or the object evolves.
No Retrospective Analysis
Prevents confirming if a new defect existed earlier or tracking its evolution over time.
Target Object
Enhancing photogrammetric measurement systems through Gaussian Splatting 8th September 2026

## Slide 5
Proposed paradigm shift
From temporal limitations to enhancement
PROBLEM STATEMENT
/
RESEARCH GAP AND OBJECTIVE
t0
Inspection Day
Object present
“Temporal Gap”
t1
Future Need
Object gone
Snapshot Limitation
Traditional photogrammetry yields a model of one specific capture session.
Inaccessibility
If new questions arise later (e.g., “was that scratch there?”), the object is often gone or remote (inaccessible).
Gaps
Sparse point clouds lose high-definition visual context, making small defect characterisation difficult without new acquisitions.
CURRENT
Static Capture
Limited Inspection
PROPOSED
Viewpoint
Synthesis
Generate renders from new viewpoints at t0
Back-in-Time
Navigable
Scene
Geometry
+
Appearance
+
Navigability
Enhanced
Inspection
Revisit and reinspect the past state
PARADIGM
SHIFT
05
Enhancing photogrammetric measurement systems through Gaussian Splatting 8th September 2026

## Slide 6
From static models to navigable 3D scenes
Free navigability, viewpoint synthesis and temporal preservation
METHODOLOGY
/
CONCEPT OF 3D SCENE
PARADIGM SHIFT
Free navigability
Unlike static photogrammetry, a 3D scene allows virtual “walkarounds” to explore perspectives that were never physically acquired by the camera.
Viewpoint synthesis
Synthetic renders can be generated from any coordinate within the scene, effectively emulating photographs taken at the preserved time t0.
Dataset augmentation
Renders belong to the same temporal state of original images. It is possible to generate an augmented dataset with views on the same temporal line.
3D SCENE
Camera Perspectives
Appearance
Temporal Coherence
Geometry
06
Enhancing photogrammetric measurement systems through Gaussian Splatting 8th September 2026

## Slide 7
A 3D scene can be defined as a digital high-fidelity representation of an object or environment in a precise temporal state.
Geometric information
Details on colour, textures, shading, lighting, and camera perspectives
Free navigation
Ray
Ray
A radiance field is a representation of light distribution in a 3D space, which captures how light interacts with surfaces and materials in the environment.
An implicit radiance field represents light distribution in a scene without explicitly defining the geometry of the scene.
NeRF
An explicit radiance field directly represents the distribution of light in a discrete spatial structure, such as a voxel grid or a set of points.
07
Explicit radiance field
METHODOLOGY
/
RADIANCE FIELD
Enhancing photogrammetric measurement systems through Gaussian Splatting 8th September 2026

## Slide 8
Gaussian Splatting for real-time navigable scenes
Optimization pipeline from sparse geometry to visual representation
GS OPTIMIZATION PIPELINE
SfM Initialization
Sparse point cloud input
3D Gaussians
Position, Covariance, Color, Opacity
Rasterisation
Real-time projection & blending
Sparse point cloud + camera alignment
μ
Learnable ellipsoids (millions)
Projection on image plane
08
METHODOLOGY
/
GS PIPELINE
Enhancing photogrammetric measurement systems through Gaussian Splatting 8th September 2026

## Slide 9
Gaussian Splatting (G) is an explicit radiance field with the advantages of implicit radiance field. It makes use of learnable 3D anisotropic Gaussians as a flexible, efficient representation. Optimized with multiview images, this differentiable pipeline merges gradient flow with explicit data storage. This hybrid approach enables real-time, high-quality rendering with reduced training time, even for complex, high-resolution scenes.
Spherical harmonics of degree l and order m
09
How spherical harmonics defines colour
METHODOLOGY
/
DETAILS ON SPHERICAL HARMONICS
Enhancing photogrammetric measurement systems through Gaussian Splatting 8th September 2026

## Slide 10
Synergistic photogrammetry-GS inspection approach
Scene-driven enrichment through virtual navigation and synthetic views
INNOVATIVE APPROACH
/
SYNERGYSTIC INTEGRATION
This procedure allows “new” images to be generated long after the object is gone.
Data acquisition
Input: Physical RGB images captured by (UAV) camera.
Standard photogrammetry.
Physical images
GS scene generation
Process: Train Gaussian Splatting model from images.
Creates navigable 3D scene.
3D-GS scene
Virtual navigation
Action: Navigate to new viewpoints not physically captured.
Render high-fidelity 2D images.
Synthetic renders
Enriched P-Cloud
Result: Synthetic views into photogrammetry pipeline.
Increases density and fills coverage gaps.
Enriched output
1
2
3
4
10
Enhancing photogrammetric measurement systems through Gaussian Splatting 8th September 2026

## Slide 11
Benefits of integrating GS into photogrammetry
INNOVATIVE APPROACH
/
BENEFITS OF INTEGRATION
11
Image-set augmentation
Renders can be added to the original set of physical images with the aim of increasing the number of available observations
Virtualisation of the photogrammetric acquisition process
Because camera positions and orientations can be explicitly controlled within the reconstructed scene, virtual image acquisition can be performed without the physical accessibility constraints associated with a physical acquisition campaign.
A
B
Enhancing photogrammetric measurement systems through Gaussian Splatting 8th September 2026

## Slide 12
Small-scale ballbar
12
Calibration
structured light project system ATOS GOM ScanBox Series 4;
The ATOS GOM calibrated according to ISO 10360–13:2021;
Length measurement error of 0.004 mm on a length of 160 mm (MPE of 34 μm);
Spherical size measurement error of 0.0045 mm on a diameter of 25 mm (MPE of 15 μm).
Instrumentation
Basler acA2500-14uc camera, with 2590 x 1942 pixels, a sensor format of 1/2.5”, pixel size measuring 2.2 × 2.2 μm, and a frame rate of 14 fps;
Basler Lens C125-0818-5M-P, focal length of 8.11 mm with a tolerance of ±5 %, an optimum working distance of 0.5 m, and an optimum magnification of 0.016.
EXPERIMENTAL SETUP
/
CASE STUDY
Enhancing photogrammetric measurement systems through Gaussian Splatting 8th September 2026

## Slide 13
Bias evaluation across measurands
13
GS scene is generated with 36 images extracted from a set of 72. Images are not random, but collected on two different camera elevations, with a relative angular distance of 20°.
Renders are generated from the 36 missing poses and a certain percentage of random digital images is used for dataset augmentation.
EXPERIMENTAL SETUP
/
AUGMENTED PHOTOGRAMMETRY
Enhancing photogrammetric measurement systems through Gaussian Splatting 8th September 2026

## Slide 14
Normalised error
14
Extra cases: physical Images are now random, but collected on two different camera elevations, with a relative angular distance of 20°.
Renders are generated from the 36 missing poses and a certain percentage of random digital images is used for dataset augmentation.
Sources of uncertainty
Reproducibility
Traceability
Resolution
always < 1 below 40% of renders
Measurement compatible with the reference
EXPERIMENTAL SETUP
/
NORMALISED ERROR
Enhancing photogrammetric measurement systems through Gaussian Splatting 8th September 2026

## Slide 15
Enriched photogrammetry: density and feature recovery
Massive density leap
Over 20x increase in point count allows for detection of small features previously missed.
Feature recovery
Bolts, rivet holes, and scratch edges clearly defined even with inaccessible or removed physical views.
Robustness verified
GS synthesised missing viewpoints to create a dense and adequate 3D dense point cloud.
15
EXPERIMENTAL SETUP
/
ENRICHED PHOTOGRAMMETRY
Enhancing photogrammetric measurement systems through Gaussian Splatting 8th September 2026

## Slide 16
Limitations and new perspective
Computational cost
GS requires high-end GPU resources (e.g., NVIDIA A100)
Static scene constraint
Object must remain perfectly static during acquisition
Limited interoperability
GS output not yet standard in metrology context
Renders can be freely used as images if within 40%?
OPEN QUESTION
16
DISCUSSION
1
2
3
Enhancing photogrammetric measurement systems through Gaussian Splatting 8th September 2026

## Slide 17
Summary key research contributions
Back-in-time repeatability
Established a novel paradigm using "3D Navigable Scenes" to enable retrospective inspection of past asset states, overcoming the temporal limitations of traditional photogrammetry.
Photogrammetry + GS synergy
Developed a synergistic workflow where Gaussian Splatting (digital) renders enrich photogrammetric reconstruction, increasing local density by ~10x and improving defect definition.
Validated traceability
Significant improvements in feature matching and reconstruction quality, validating the method for safety-critical LVS inspection. GS can serve as standalone inspective technique.
ACKNOWLEDGMENTS
Quality Engineering and Management Group
Dept. of Management & Production Eng.
Mind4Lab
Politecnico di Torino
Q & A Session
17
CONCLUSIONS
Enhancing photogrammetric measurement systems through Gaussian Splatting 8th September 2026

## Slide 18
Enhancing photogrammetric measurement systems through Gaussian Splatting
Mattia Trombini, Giacomo Maculotti Gianfranco Genta, Maurizio Galetto
Presenting author Mattia Trombini Dept. of Management and Production Eng., Politecnico di Torino, Italy mattia.trombini@polito.it
Firenze, 8th September 2026

## Slide 19
SEMI-AUTOMATIC DETECTION
Scene comparison
Direct comparison between “pristine” (t0) and “defective” (t1) scenes using geometric and chromatic differences.
Detection logic
Oxidation points: detected via gradient map + density increase. Scratches: detected via area sampling + increase density + decreased volume.
Semi-automatic workflow
Automates the identification of potential anomalies, reducing operator workload while keeping human-in-the-loop for final verification.
Semi-automatic defect detection
19
Supplementary material
BACKUP
/
BRAKE DISC

## Slide 20
20
Supplementary material
BACKUP
/
CONCEPT OF “SPLATTING”
“Splatting”

## Slide 21
Dataset
200 ground-truth images (3840x2160 pixels)
30 localised renders
Case A: baseline P
Case B: enriched P + 30 G renders
Instrumentation
Matrice 350RTK
Zenmuse L2 high-resolution camera
Agisoft Metashape© for P
Python with PyTorch framework and custom CUDA © for G
System for Image-Based Rendering (SIBR) for render extraction
A portion of the surface shows visible damage defined as a bump consistent with the impact caused by the collision with a flock of birds (bird strike).
21
Supplementary material
BACKUP
/
RESULTS ON ENGINE LIP
Experimental setup – engine lip

## Slide 22
Point cloud is projected from 3D onto the 2D image plane where the image of the bump lies.
Points are superimposed onto the image, creating a density map where the colour represents the computed distances with respect to the theoretical inner surface.
Case A
Case B
22
Supplementary material
BACKUP
/
RESULTS ON ENGINE LIP
Experimental setup – engine lip

## Slide 23
Dataset
260 ground-truth images (3840x2160 pixels)
G.1 scene from 260 images
G.2 scene from 253 images
G.3 scene from 248 images
Case A.1: baseline P
Case B.1.1: enriched P + 15 G.1 renders
Case B.1.2: enriched P + 15 G.2 renders
Case B.1.3: enriched P + 15 G.3 renders
Instrumentation
Matrice 350RTK
Zenmuse L2 high-resolution camera
Agisoft Metashape© for P
Python with PyTorch framework and custom CUDA © for G
System for Image-Based Rendering (SIBR) for render extraction
23
Supplementary material
BACKUP
/
RESULTS ON FUSELAGE LOG
Experimental setup – fuselage log

## Slide 24
The enhancement of local portions of the reconstructed domain is relevant in increasing local density.
Collecting renders in the defect surroundings allows for a better definition of all the local parts of the object, with all the constituents (e.g., bolts, holes, defects, etc.) more clearly distinguishable.
PSNR (↑): range [0; ∞]
SSIM (↑): range [-1; 1]
LPIPS (↓): range [0; 1]
Density within the defective region
By selectively removing images of the defective area, the experiment simulates challenging inspection conditions and evaluates whether G scene can generate accurate renders for photogrammetric enrichment.
24
Supplementary material
BACKUP
/
RESULTS ON FUSELAGE LOG
Experimental setup – fuselage log