## Slide 1: A Semi-Supervised Framework for Optimisation-Based Label Inference in Remaining Useful Life Prediction
Joseph Cupit, joseph.cupit@postgrad.manchester.ac.uk
Dr Dongda Zhang, dongda.zhang@manchester.ac.uk
Department of Chemical Engineering
The University of Manchester

## Slide 2
1. Background
2. Methodology
3. Results & Discussion
4. Conclusions
2
Outline

## Slide 3
1. Background
3

## Slide 4
4
1. Background
Utilising Abundant Industrial Datasets
Modern industrial equipment is continuously monitored using networks of sensors
These sensors generate large volumes of operational data
Sensor data can reveal degradation patterns and help anticipate equipment failure
Predictive maintenance can reduce:
Unplanned downtime
Unexpected maintenance costs
Unnecessary interventions
Equipment degradation is tracked using condition-based Key Performance Indicators (KPIs)
Remaining Useful Life (RUL) quantifies the time remaining before a failure condition is reached

## Slide 5
5
1. Background
Machine Learning for Predictive Maintenance
Sensor data form multivariate time series describing how equipment condition evolves
RUL prediction requires a model that can learn patterns across time
Long Short-Term Memory (LSTM) networks retain relevant information from earlier timesteps
Using supervised learning, an LSTM maps a window of sensor data to the current RUL

## Slide 6
6
1. Background
Why Reliable RUL Labels Are Scarce
Supervised RUL models require sensor trajectories with corresponding RUL labels
Reliable labels require the eventual failure to be known
In practice, equipment is usually maintained before failure is observed
Most operational trajectories cannot be labelled directly
Only a small labelled subset is available for supervised training

## Slide 7
7
1. Background
Making the Most of Existing Data
Additional run-to-failure trajectories are costly and time-consuming to collect
Existing unlabelled data still capture useful degradation behaviour
Semi-supervised learning offers a way to combine them with limited labelled data
Can unlabelled trajectories improve RUL prediction when labelled data are scarce?

## Slide 8
2. Methodology
8

## Slide 9
9
2. Methodology
Turning Unlabelled Trajectories into Useful Training Data
Objective: transform unlabelled trajectories into useful supervised training data
Approach: treat their unknown RUL labels as optimisable variables
1. Initial label guess
2. Optimisation
3. Final model

## Slide 10
10
2. Methodology
Step 1: Generating Initial RUL Estimates
To avoid random initialisation, data-driven RUL estimates are generated
A preliminary LSTM is trained on the available labelled batches
The model estimates the end-of-batch RUL for each unlabelled batch
These estimates provide an informed starting point for label optimisation

## Slide 11
11
2. Methodology
Step 2: Label Inference as an Optimisation Problem
Optimisation uses one end-of-batch RUL value for each unlabelled batch
One complete set of proposed RUL values forms a candidate solution
Each candidate-labelled dataset is used to train a small evaluation LSTM
Validation WAPE on known labelled data provides the candidate’s fitness score
Key assumption: Shared degradation behaviour allows validation performance to reflect candidate-label quality

## Slide 12
12
2. Methodology
Step 2: The Genetic Algorithm
Initialise the population of candidate label sets with small mutations to preliminary LSTM estimates
Evaluate each candidate using validation WAPE as its fitness score
Retain the five candidates with the lowest WAPE through elitism
Mutate random high-performing candidates to generate the next population
Repeat for 50 generations or until convergence, then select the candidate with the lowest WAPE

## Slide 13
13
2. Methodology
Step 3: Training the Final Model on the Expanded Dataset
Optimised RUL labels make previously unlabelled batches available for supervised training
These batches are combined with the original labelled data to create an expanded training dataset
A new final LSTM is trained from scratch on the expanded dataset
The final model is evaluated on independent labelled test batches using WAPE

## Slide 14
14
2. Methodology
Experimental Design
Each experiment infers RUL labels for 50 unlabelled batches
Labelled-data availability is varied from 1 to 25 batches (2%-50%)
Each availability level is repeated across 10 random labelled-data splits
A baseline LSTM is trained on the same labelled subset without inferred labels
Both models are evaluated using WAPE on independent labelled test batches

## Slide 15
15
2. Methodology
Evaluating Label Inference Across Contrasting Datasets
PtPM
Industrial experimental dataset
Compressed air filtration
Physical experiment
3 sensor variables
Simple, well-defined degradation
C-MAPSS
NASA benchmark dataset
Turbofan engine degradation
Simulation
21 sensor variables
Complex, interacting degradation
The two datasets test how effective label inference is as degradation complexity increases

## Slide 16
3. Results & Discussion
16

## Slide 17
17
3. Results & Discussion
Unlabelled Data Improves RUL Prediction
Label-scarce PtPM case: only 2 labelled batches available
Adding 50 batches with inferred labels reduces test WAPE from 72.5% to 36.4%
The framework-trained LSTM follows true RUL trajectories much more closely
Notes: One minor clarity point: the bar chart shows the six-property G-to-G model, while the heading above distinguishes the single-property G-to-G result 𝑅^2=0.85from the multi-property result 𝑅^2=0.87. That distinction is present, but make sure you state it verbally.

## Slide 18
18
3. Results & Discussion
PtPM: Largest Gains Under Label Scarcity
Inferred labels reduce WAPE at 5 of 7 labelled-data levels
Benefits are greatest with 2%-10% labelled data
Benefits reduce as more labelled data are available
Notes: One minor clarity point: the bar chart shows the six-property G-to-G model, while the heading above distinguishes the single-property G-to-G result 𝑅^2=0.85from the multi-property result 𝑅^2=0.87. That distinction is present, but make sure you state it verbally.

## Slide 19
19
3. Results & Discussion
C-MAPSS: Consistent Gains Beyond Extreme Scarcity
Inferred labels reduce WAPE at 6 of 7 labelled-data levels
Improvements persist from 4% to 50% labelled data
At 2%, inferred labels increase WAPE
Notes: One minor clarity point: the bar chart shows the six-property G-to-G model, while the heading above distinguishes the single-property G-to-G result 𝑅^2=0.85from the multi-property result 𝑅^2=0.87. That distinction is present, but make sure you state it verbally.

## Slide 20
20
3. Results & Discussion
Comparing Performance
Label inference is most valuable when labelled data are scarce but sufficient to guide reliable optimisation
PtPM: larger gains under label scarcity
C-MAPSS: steadier gains once extreme scarcity is avoided
Inferred labels reduce WAPE in 11 of 14 tested settings
Notes: One minor clarity point: the bar chart shows the six-property G-to-G model, while the heading above distinguishes the single-property G-to-G result 𝑅^2=0.85from the multi-property result 𝑅^2=0.87. That distinction is present, but make sure you state it verbally.

## Slide 21
4. Conclusion
21

## Slide 22
22
4. Conclusion
Making Unlabelled Data Useful for RUL Prediction
The framework infers RUL labels for unlabelled trajectories
Converts previously unused trajectories into useful supervised training data
Improves RUL prediction in most scenarios across two datasets
Provides the greatest value when labelled data are scarce
Allows predictive maintenance models to use more of the available operational data
Unlocks value from industrial sensor data already being collected
Notes: One minor clarity point: the bar chart shows the six-property G-to-G model, while the heading above distinguishes the single-property G-to-G result 𝑅^2=0.85from the multi-property result 𝑅^2=0.87. That distinction is present, but make sure you state it verbally.

## Slide 23: Thank You!
Croda
Dr Elizabeth Dickinson
Dr James Birbeck
Joseph Cupit, joseph.cupit@postgrad.manchester.ac.uk
Dr Dongda Zhang, dongda.zhang@manchester.ac.uk