## Slide 1
HUMAN SIDE OF TECHNOLOGY
Adaptive Particle MCMC for non-linear battery state-space models
1
Edvinas Juozapaitis1, Robertas Alzbutas1,2
1 Kaunas University of Technology, Department of Applied Mathematics
2 Lithuanian Energy Institute
edvinas.juozapaitis@ktu.lt
Florence, 2026

## Slide 2
Introduction (1):
Li-ion battery context
Li-ion batteries are still the most used for energy storage, electronics, EVs, etc.
Problem
Battery aging leads to reliability and sustainability issues
Solution
Estimate battery states using real-time data to monitor battery health
Battery management systems (BMS) collect only key data: current, voltage, etc.
Specialized techniques required to estimate battery states online and determine condition
  State of Charge (SOC); State of Health (SOH); State of Power (SOP); State of Energy (SOE); …

## Slide 3
Introduction (2):
Battery state estimation techniques
Simple methods: coulomb counting (SOC), power integral (SOE), incremental capacity experiments (SOH)
  low computation; intuitive setup
  error accumulation; sensitive to initial conditions
Electrochemical models: PDE-based material level simulations
  high accuracy; interpretable physical parameters
  complex parameter space; costly identification
State-space models: data-driven statistical filters for modelling cells
  stochastically handled uncertainty; online Bayesian updating
  data-hungry; simplified physical interpretation

## Slide 4
Particle Filtering (1):
State-space model formulation
Definition
Hidden state:
Initial distribution
Transition distribution
Observations:
Conditional distribution
Objective
Filtering distribution
Prediction step
Update step
Problem
  Prediction integral is intractable for a non-linear system
Solution
  Approximate the filtering distribution using an empirical measure

## Slide 5
Particle Filtering (2):
Empirical approximation
Objective
Approximate filtering distribution using weighted particles:
Weight updating
Choosing a simple proposal distribution: , weight updating becomes:
Unbiased marginal likelihood estimate
Particles:
Normalized weights:
Dirac mass at :

## Slide 6
Particle Filtering (3):
Particle resampling
Problem
Weight degeneracy:
Solution
Monitor effective sample size
Resample when

## Slide 7
Particle MCMC (1):
Parameter inference problem
Objective
Compute posterior distribution of unknown parameters given observations
Parameter posterior distribution:
Problem
Intractable marginal likelihood :
Solution
Use estimate from PF:

## Slide 8
Particle MCMC (2):
Particle Marginal Metropolis-Hastings
Procedure
Initialization
Choose initial parameter vector
Run PF to compute marginal likelihood estimate
For iteration :
Propose parameter candidate
Compute likelihood estimate for parameter candidate using PF
Calculate acceptance probability
Generate . If , , otherwise

## Slide 9
Application in Battery SSM (1):
Equivalent circuit model (2nd-order Thevenin)
Current data used as input
Parameter space
Hidden states |  |  | 
Observations |  |  | 
Hidden states |  |  | 
Observations |  |  | 

## Slide 10
Application in Battery SSM (2):
Standard PMCMC fails
Issues
High dimensionality
Parameter correlations
Low acceptance rate
Complexity

## Slide 11
Adaptive PMCMC:
3-phase strategy
Phase 1 - Exploration | Phase 2 – Likelihood Annealing | Phase 3 – Data Annealing
No particle resampling | Standard resampling | Standard resampling
Data fraction: | Data fraction: | Data fraction:
Flat likelihood function. Builds a global empirical covariance | Posteriors transition from prior-dominated to data-dominated | Increases the information content of the likelihood, sharpening posteriors
Phase 1 - Exploration | Phase 2 – Likelihood Annealing | Phase 3 – Data Annealing
No particle resampling | Standard resampling | Standard resampling
 | Posteriors transition from prior-dominated to data-dominated | Increases the information content of the likelihood, sharpening posteriors

## Slide 12
Results (1):
OCV curve + capacity estimate
Capacity mean estimate: 104.197 Ah
SOH estimate: 99.24%

## Slide 13
Results (2):
SOC estimate
SOC estimate obtained using the inverse of function :
No RC components included in model

## Slide 14
[Alternative Approach] Electrochemical Model (1):
SP+ model formulation
Objective
Model each electrode as a single spherical particle
Simplifies spatial variation of lithium concentrations
Assumes uniform reaction kinetics
Governing equations
Radial diffusion PDE:
Reduction to ODE (parabolic profile approximation):
Surface state of charge:
Open circuit voltage:
Full details in (Dabulytė-Bagdonavičienė et al., 2026)

## Slide 15
Electrochemical Model (2):
Parameter identification
Cell geometry |  | Effective electrode area
 |  | Electrode thickness
 |  | Electrode porosity
Particle structure |  | Active material particle radius
Diffusion properties |  | Solid-phase diffusion coefficient
Cell geometry |  | Effective electrode area
 |  | Electrode thickness
 |  | Electrode porosity
Particle structure |  | Active material particle radius
Diffusion properties |  | Solid-phase diffusion coefficient
Objective
Identify uncertain model parameters
Minimize error between modelled voltage and collected voltage data:
Parameter bounds based on literature
Problem
Full optimization computationally expensive
Solution
Use sensitivity analysis to determine parameter influence

## Slide 16
Electrochemical Model (3):
Sensitivity analysis
Procedure
Determine relationship between parameters and output
Regression on raw data yields poor fit ()
Ranked data regression shows good fit ()
Monotonic non-linear
Select sensitivity measures:
Rank-based indices
Partial rank correlation coefficients (PRCC); Standardized rank regression coefficients (SRRC)
Global sensitivity measures
Smirnov indices; Sobol first and total order indices
Most impactful:
Moderate impact:
Negligible impact:

## Slide 17
Electrochemical Model (4):
OCV curve + uncertainty measure
Voltage uncertainty at 50% charge
Visible outliers caused by instabilities

## Slide 18
Closing remarks (1):
Method comparison
 | Adaptive PMCMC |  | Single Particle +
+ | Stable adaptation over 3 phases | + | Computationally efficient
 | Simple or automated tuning |  | Preserves interpretable electrochemical physics
 | No assumptions about battery | - | Requires knowledge of battery specifics
 | Verified using varied battery data |  | Highly sensitive and unstable given wider parameter intervals
- | Neglects auxiliary BMS data (e.g., temperature) |  | Neglects auxiliary BMS data (e.g., temperature)
 | Long computation times make online application infeasible |  | 

## Slide 19
Closing remarks (2):
Future work
Implement other BMS sensor data for more accurate state estimation and battery health monitoring
Temperature; Humidity; Pressure; Vibrations; …
Improve Adaptive PMCMC computation speed for online application
Implementing parallelization techniques, cloud computing
Validate both methods using diverse battery configurations and cycling conditions
Requires data of varying physical/chemical setups during varied usage dynamics
Continuously monitor an aging battery to predict remaining useful life (RUL)

## Slide 20
References
Dabulytė-Bagdonavičienė, J., Vaidelienė, G., Juozapaitis, E., & Alzbutas, R. (2026). Probabilistic Sensitivity Analysis of a Nonlinear Electrochemical Model as a Virtual Replica for Lithium-Ion Battery Design Under Uncertainty. Mathematics, 14(12), 2162. https://doi.org/10.3390/math14122162
Shen, M., & Gao, Q. (2019). A review on battery management system from the modeling efforts to its multiapplication and integration. International Journal of Energy Research, 43(10), 5042–5075. https://doi.org/10.1002/er.4433
Chopin, N., & Papaspiliopoulos, O. (2020). An Introduction to Sequential Monte Carlo. Springer International Publishing. https://doi.org/10.1007/978-3-030-47845-2
Li, J., Wang, D., Deng, L., Cui, Z., Lyu, C., Wang, L., & Pecht, M. (2020). Aging modes analysis and physical parameter identification based on a simplified electrochemical model for lithium-ion batteries. Journal of Energy Storage, 31, 101538. https://doi.org/10.1016/j.est.2020.101538
Laue, V., Röder, F., & Krewer, U. (2019). Joint structural and electrochemical modeling: Impact of porosity on lithium-ion battery performance. Electrochimica Acta, 314, 20–31. https://doi.org/10.1016/j.electacta.2019.05.005
Kang, J., Gong, Z., Wang, J. V., Chen, W., Wang, Q., Fan, Y., & Huang, B. (2025). A novel method of parameter identification for electrochemical models of LiFePO4 batteries using parallel computing and multi-objective optimization. Journal of Energy Storage, 122, 116662. https://doi.org/10.1016/j.est.2025.116662
Jafari, M., Khan, K., & Gauchia, L. (2018). Deterministic models of Li-ion battery aging: It is a matter of scale. Journal of Energy Storage, 20, 67–77. https://doi.org/10.1016/j.est.2018.09.002

## Slide 21
Appendix (1):
PMCMC hyperparameter tuning
Particle number | Proposal scaling factor
Linearly increases comp. time; Controls the variance of the unbiased likelihood estimate | Applies multiplicative scaling to the empirical covariance; Aggressive scaling keeps the chain mobile
Linearly increases comp. time; Controls the variance of the unbiased likelihood estimate | Applies multiplicative scaling to the empirical covariance; Aggressive scaling keeps the chain mobile

## Slide 22
Appendix (2):
PMCMC OCV curve results – static images
Phase 1 | Phase 2 | Phase 3